## Slide 1
Marine Litter Hazard Assessment
in the Sardinian Sea
HHE Data Science Laboratory · Politecnico di Milano
MSFD Descriptor 10 · ISPRA Data 2020–2023
6 BEACHES
41 surveys
14 STATIONS
710 observations
4 YEARS
2020–2023

## Slide 2
Research Question
How is marine litter hazard spatially distributed along the Sardinian coast,
and what temporal patterns emerge from ISPRA monitoring data (2020–2023)?
WHY IT MATTERS
Mediterranean: 7% of global marine plastic, <1% of ocean surface
Sardinia: 1,849km coastline
3.5M tourists/year
Fragile marine ecosystems
(Posidonia, coralligenous)
KNOWLEDGE GAP
No unified spatial hazard map for Sardinian coast
ISPRA data collected since 2015 but never spatially analyzed at sub-regional scale
OUR APPROACH
IPCC hazard framework at sub-regional scale
IDW interpolation on 10km grid
2 compartments:
beach + floating litter

## Slide 3
01 — DATA
Sources · Structure · Cleaning

## Slide 4
ISPRA MSFD Monitoring Data
MODULO 4 · Beach Litter
6
beaches
41
surveys
2020–2023
years
2 surveys/year (spring + autumn)
Metric: items / 100m transect
EU JointListCategory standard
6 sites along Sardinian coast
MODULO 2BIS · Floating Litter
14
stations
710
observations
2021–2023
years
Bimonthly surveys
Metric: observations per station
Ship-based visual transect
Offshore monitoring network

## Slide 5
Data Harmonization
Schema differences between 2020 and 2023 file formats
Issue | 2020 Format | 2023 Format | Solution
Survey ID | SampleID | CodiceCampionamento | → survey_id
Item count | NumeroItems | NumeroOggetti | → n_items
Transect length | Lunghezza | LunghezzaTransetto | → transect_m
Material names | Italian (Polimeri artificiali) | English (Artificial polymer) | → normalized EN
✓ All files: transect_m = 100m (fixed MSFD protocol)
✓ Missing lat/lon: filled from known station coordinates per beach_id
Raw XLS files
pandas normalize()
Unified CSV

## Slide 6
02 — EXPLORATORY ANALYSIS
Beach litter · Floating litter · Patterns

## Slide 7
Beach Litter Trend per Stazione (2020–2023)
Key Findings
▶ Oristano: 539 items/100m (highest)
▶ Alghero: 508 items/100m
▶ S.Teodoro: 58 items/100m (lowest)
▶ EU threshold: 150 items/100m
▶ 4/6 beaches exceed threshold
▶ West coast > East coast
⚠ West coast significantly above EU threshold

## Slide 8
Composition & Source Attribution
Top 10 categories (JointListCategory)
Source attribution (land / sea / fishing)

## Slide 9
Floating Litter — Composition & Seasonality
69% of floating litter is artificial polymer (plastic). Peak obs: autumn/winter — consistent with seasonal wind/current patterns.

## Slide 10
03 — SPATIAL HAZARD INDEX
Methodology · Results · Hotspots

## Slide 11
Hazard Index — Methodology
1
NORMALIZE
Min-max score 0–1 per station. Global normalization across all years.
2
INTERPOLATE
IDW on 10km grid. Radius 1.0° beach, 1.2° floating. 289 grid cells.
3
COMPOSITE
Hazard = mean(beach, floating) per cell. Equal weights.
4
CLASSIFY
5 classes from Very Low to Very High.
Very Low <0.2
Low 0.2–0.4
Medium 0.4–0.6
High 0.6–0.8
V.High >0.8

## Slide 12
Composite Hazard Index — Sardinia 2020–2023
Left: beach litter score · Center: floating litter score · Right: composite hazard index | ● beach stations · ▲ floating stations

## Slide 13
Temporal Evolution — Hazard Index 2020–2023

## Slide 14
Key Findings
HOTSPOTS
🔴 West coast (Alghero–Oristano): highest hazard
🔴 Oristano Is Arenas: beach score 1.00
🟠 Alghero Lido: beach score 0.94
🟢 San Teodoro La Cinta: score 0.00 (lowest)
🔵 3 grid cells: HIGH class (hazard >0.6)
539
items/100m (Oristano peak)
PATTERNS
59% floating litter = artificial polymer
Beach litter peaks: west coast year-round
Floating peaks: autumn/winter
4/6 beaches exceed EU 150 items/100m threshold
Trend: apparent reduction 2020→2021 partly methodological
4/6
beaches above EU threshold

## Slide 15
Limitations & Next Steps
⚠ LIMITATIONS
6 beach stations → sparse, IDW smooths aggressively
Seafloor compartment missing (no MSFD module locally)
Score is relative, not absolute scale
2020 beach-only ≠ 2021–23 composite
obs count ≠ standardized density
→ NEXT STEPS
Retrieve seafloor data (MEDITS) from ISPRA DB
Add 3rd compartment → complete hazard index
Replace grid with coastal administrative segments
Validate vs citizen science beach cleanup data
Final presentation + policy implications (Phase 4)

## Slide 16
Thank You
GitHub: daniele22-u/hhe-labsardinia
Data: ISPRA — Sistema Nazionale per la Protezione dell'Ambiente
Framework: EU Marine Strategy Framework Directive (MSFD) · Descriptor 10
HHE Data Science Laboratory · Politecnico di Milano · 2026